## Slide 1: Unit II
IoT Architecture

## Slide 2
Standardizing the IoT
Smart objects produce large volumes of data. This data needs to be managed, processed, transferred and stored securely. Standardization is key to achieving universally accepted specifications and protocols for true interoperability between devices and applications.
The use of standards:
ensures interoperable and cost-effective solutions
opens up opportunities in new areas
allows the market to reach its full potential
The more things are connected, the greater the security risk. So, security standards are also needed to protect the individuals, businesses and governments which will use the IoT.

## Slide 3
European Telecommunications Standards Institute M2M/oneM2M
The main ETSI IoT standardization activities are conducted at radio layer in 3GPP (LTE-M, NB-IoT and EC-GSM-IoT) and at service layer in oneM2M. A wide range of technologies work together to connect things in the Internet of Things (IoT). ETSI is involved in standardizing many of these technologies:

## Slide 4
Smart Machine-to-Machine (M2M) communications
ETSI is one of the founding partners in oneM2M, the global standards initiative that covers requirements, architecture, Application Programming Interface (API) specifications, security solutions and interoperability for M2M and IoT technologies.
IoT Semantic Interoperability
SAREF is our Smart Applications REFerence ontology that allows connected devices to exchange semantic information in many applications’ domains.

## Slide 5
Context Information Management (NGSI-LD)
ETSI ISG CIM specifies protocols (NGSI-LD API) running ‘on top’ of IoT platforms and allowing exchange of data together with its context, this includes what is described by the data, what was measured, when, where, by what, the time of validity, ownership, and others.
This is dramatically extending the interoperability of applications, helping smart cities (and other areas such as Smart Agriculture and Smart Manufacturing) to integrate their existing services and enable new third-party services.

## Slide 6
Applications in the IoT
Within ETSI we are addressing various applications of IoT/M2M technology:
Smart appliances
Smart grids and meters
Smart cities – including networking, energy efficiency and accessibility
Smart Energy, Smart Environment, Smart Building, Smart Industry and Manufacturing, Smart Agri-Food, eHealth and Ageing-Well, Wearables, Smart Water, Smart Lift and Smart Escalators
D. eHealth
  Telemedicine and the Internet Clinic
  Medical implants
  Body Area Networks
  Pandemic protection, contact tracing

## Slide 7
E. Intelligent Transport Systems – including telematics and all types of communications in vehicles, between vehicles and between vehicles and fixed locations. We also address the use of Information and Communications Technologies for rail, water and air transport, including navigation systems.
F. Wireless Industrial Automation – standards for radio equipment to be used in factories

## Slide 8
oneM2M
The oneM2M global organization creates technical specifications to ensure that Machine-to-Machine Communications can effectively operate on a worldwide scale.
Seven of the world's leading information and communications technology (ICT) Standards Development Organizations (SDOs) launched in July 2012 a new global organization to ensure the most efficient deployment of machine-to-machine (M2M) communications systems.

## Slide 9
ETSI M2M high-level architecture

## Slide 10
This high-level architecture is a combination of both a functional and topological view showing some functional groups (FG) clearly associated with pieces of physical infrastructure (e.g. M2M Devices, Gateways).
There are two main domains, a network domain and a device and gateway domain.
The boundary between these conceptually separated domains is the topological border between the physical devices and gateways and the physical communication infrastructure (Access network).

## Slide 11
The Device and Gateway Domain contains the following functional/topological entities:
M2M Device:
This is the device of interest for an M2M scenario, for example, a device with a temperature sensor.
An M2M Device contains M2M Applications and M2M Service Capabilities.
An M2M device connects to the Network Domain either directly or through an M2M Gateway:
• Direct connection: The M2M Device is capable of performing registration, authentication, authorization, management, and provisioning to the Network Domain. Direct connection also means that the M2M device contains the appropriate physical layer to be able to communicate with the Access Network.

## Slide 12
• Through one or more M2M Gateway: M2M device does not have the appropriate physical layer, compatible with the Access Network technology, and therefore it needs a network domain proxy.
Moreover, a number of M2M devices may form their own local M2M Area Network that typically employs a different networking technology from the Access Network. The M2M Gateway acts as a proxy for the Network Domain and performs the procedures of authentication, authorization, management, and provisioning. An M2M Device could connect through multiple M2M Gateways

## Slide 13
M2M Area Network:
This is a local area network (LAN) or a Personal Area Network (PAN) and provides connectivity between M2M Devices and M2M Gateways.
Typical networking technologies are IEEE 802.15.1 (Bluetooth), IEEE 802.15.4 (ZigBee, IETF 6LoWPAN/ROLL/CoRE), MBUS, KNX (wired or wireless) PLC, etc.
M2M Gateway:
The device that provides connectivity for M2M Devices in an M2M Area Network towards the Network Domain.
The M2M Gateway contains M2M Applications and M2M Service Capabilities.
The M2M Gateway may also provide services to other legacy devices that are not visible to the Network Domain.

## Slide 14
The Network Domain contains the following functional/topological entities:
 Access Network:
 This is the network that allows the devices in the Device and Gateway Domain to communicate with the Core Network.
 Example Access Network Technologies are fixed (xDSL, HFC) and wireless (Satellite, GERAN, UTRAN, E-UTRAN W-LAN, WiMAX).
 Core Network:
 Examples of Core Networks are 3GPP Core Network and ETSI TISPAN Core Network. It provides the following functions:
• IP connectivity.
• Service and Network control.
• Interconnection with other networks.
• Roaming.

## Slide 15
M2M Service Capabilities:
 These are functions exposed to different M2M Applications through a set of open interfaces.
 These functions use underlying Core Network functions, and their objective is to abstract the network functions for the sake of simpler applications.
M2M Applications:
 These are the specific M2M applications (e.g. smart metering) that utilize the M2M Service Capabilities through the open interfaces
Network Management Functions:
These are all the necessary functions to manage the Access and Core Network (e.g. Provisioning, Fault Management, etc.).

## Slide 16
M2M Management Functions:
 These are the necessary functions required to manage the M2M Service Capabilities on the Network Domain.
 There are two M2M Management functions:
M2M Service Bootstrap Function (MSBF): The MSBF facilitates the bootstrapping of permanent M2M service layer security credentials in the M2M Device or Gateway and the M2M Service Capabilities in the Network Domain.
M2M Authentication Server (MAS): This is the safe execution environment where permanent security credentials such as the M2M Root Key are stored.

## Slide 17
OneM2M Functional Architecture

## Slide 19
Application Entity (AE) represents an instantiation of application logic for end-to-end M2M solutions. Each AE is identified with a unique AE-ID. For example, an AE can be an instance of application for fleet tracking, remote blood sugar monitoring, power metering, etc.
Common Services Entity (CSE) represents an instantiation of a set of Common Services Functions of the M2M environments, where each CSE is identified with a unique CSE-ID. Such service functions are exposed to other entities through reference points, where one of them is used for accessing Underlying Network Service Entities. Service functions offered by CSE include Data Management, Device Management, M2M Subscription Management and Location Services. Such "sub-functions" may be logically and informatively conceptualized as Common Services Functions (CSFs).
The normative Resources which implement the service functions in a CSE can be mandatory or optional.

## Slide 20
Network Services Entity (NSE) is an underlying entity which provides services from the underlying network to CSEs. However, even though underlying networks provide data transport services between entities in the OneM2M System, such data transport services are not included in the NSE. NSE provides services of device management, location services and device triggering.
OneM2M supports four basic types of Nodes:
Application Service Node, Application Dedicated Node, Middle Node and Infrastructure Node.
As functional objects, such Nodes may or may not be mapped to physical objects.

## Slide 21
Application Service Node (ASN) contains one CSE and contains at least one AE. There may be zero or more ASNs in the Field Domain of an M2M System. An ASN may communicate with either exactly one Middle Node or exactly one Infrastructure Node. An ASN also communicates with NSE. Physically, an ASN could reside in an M2M Device.
Application Dedicated Node (ADN) contains at least one AE and does not contain a CSE. There may be zero or more ADNs in the Field Domain of an M2M System.
An ADN communicates with a Middle Node or an Infrastructure Node. Physically, an ADN could reside in a constrained M2M Device.

## Slide 22
Middle Node (MN) contains one CSE and zero or more AEs. There may be zero or more MNs in the Field Domain of an M2M System. A MN communicates with
ASNs, ADNs, NSEs, other MNs and Infrastructure Nodes. Physically, a MN could reside in an M2M Gateway.
Infrastructure Node (IN) contains one CSE and contains zero or more AEs. There is exactly one logical IN in the Infrastructure Domain per OneM2M Service Provider of an M2M System. It may contain CSE functions not applicable to other node types. An IN communicates with one or more MNs, one or more ASNs, one or more ADNs, NSEs and INs of other M2M Systems. Physically, an Infrastructure Node could reside in an M2M Service Infrastructure.

## Slide 23
Another type of Nodes is possible, a Non-oneM2M Node (NoDN). It does not contain any of the OneM2M Entities. Physically, NoDNs are devices attached to the OneM2M system for interworking purposes, including management. These nodes reside in Field Domain.
Two general kinds of OneM2M Nodes are supported, a Common Services Entity-Capable Node and a Non-Common Services Entity-Capable Node. A Common Services Entity-Capable Node is a functional entity that contains one CSE and zero or more AEs. The Application Service Node and Middle Node are examples of a Common Services Entity-Capable Nodes.
CSEs resident in different Nodes could not be identical and are dependent on the services supported by the CSE in that Node. A Non-Common Services Entity-Capable Node is a functional entity that contains one or more AEs and no CSE. The Application Dedicated Node is an example of a Non-Common Services Entity-Capable Node.